## Slide 1: Design, model and build a USAR robot platform
Notes: Cover & End Slide Option
Replace the background image: Right-click on the slide, then choose Format Background and select Picture or texture fill. Select a new picture of your choice.
Remember to add an image attribution for e.g., Photo by Stefan Els.

## Slide 2: Design, model and build a USAR robot platform
What is USAR?
What is a Load Intuitive Module (LIM)?
Objectives:
  Model the LIM kinematics
  Design and build a robot using LIMs
  Validate the model using the robot
Introduction & Objectives
Notes: Introduce the topic and the speaker
Give a short overview of the presentation
Give the background to the topic - context is important
Clear problem statement and description of the objectives
Summary of the approach or strategy that was or will be used
List objectives
Comment on progress

## Slide 3: Design, model and build a USAR robot platform
Wilson Haskel Buchannan Powrie
Past Projects
Notes: List previous projects, include graphics for a timeline
Describe problems each faced, and successes
Describe how my project differs

## Slide 4: Design, model and build a USAR robot platform
Mathematical model in MATLAB
  Kinematics, forces, moments solved simultaneously
  Output angular accelerations as a function of torque input
  Limited to two dimensions
Simulation in Drake
  Software used and maintained by MIT
  Import CAD model from Onshape
  Allows for customisation of inertia, friction etc.
Mathematical Model and Simulation
Notes: Describe process for mathematical model –set of equations, substitution etc.
Describe process for simulation – pydrake – sdformat – onshape etc. include video
Discuss potential limitations

## Slide 5: Design, model and build a USAR robot platform
Physical device has been built and tested
  Manually filed d-shafts to avoid MMW queue
  Uses JGY-370 gearbox motors for high torque and self-locking ouput
Uses sliders to control each motor individually
Can climb stairs
  LIMs must move simultaneously, if one falls behind the other then it struggles to catch up.
Physical device
Notes: Discuss construction of physical device – use different motors/gearbox – laser cut parts – file shafts manually
Discuss controller – design – components
Discuss testing – success, limitations, video

## Slide 6: Design, model and build a USAR robot platform
Motors use a 12V power supply, which is considered safe to touch.
Gears are enclosed within the frame of the LIMs.
Power to motors can be easily shutoff.
Power should be shutoff when handling the device
Motor burnout:
  Motors cannot maintain stalling current for more than a few seconds
  Stalling is common during imbalanced climbing
Safety
Notes: Safety information – keep voltages low, avoid moving parts, disconnect device before handling it - fingers

## Slide 7: Design, model and build a USAR robot platform
Improving device
  Increase torque
Recording device
  OpenCV with aruco markers
Validate model
  Likely need to update model
Design new device
  Inform design with mathematical model
  Test concepts in simulation
Build new device
Future work
Notes: Improve device – higher gear ratio, current feedback, encoder feedback difficult ti implement
Record device – OpenCV with Aruco tags, start recording soon
Validate models – project objectives complete!
Design new device, informed by model and test concepts with simulation
Build new device – better parts – herringbone gears and bal bearings

## Slide 8: Design, model and build a USAR robot platform
Learnt from previous work
Modelled device mathematically and in simulation
Built working device
Next: Track motion of device
Conclusion
Notes: Load intuitive moduls are an